Plan for tutorial:

- Screenshot all steps taken
- Could offer a brief explanation on zooming out and navigating around the screen (not sure if this is overkill)
- I could put in my data from python as a .csv file so people who use the tutorial can compare the data they made?
- Base tutorial off each screenshot.

4	Simulation using Aquarius

4.1.1	Lauch editor
Copy and paste
4.1.2	Define device geometry
Directly below the menu bar, left-click the square
###insert "C:\Users\isaac\Downloads\KuasaSemi\aquarius-docs\static\img\examples\PN junction\p_region\01.png"
- Position the cursor on the canvas to draw a rectangular shape:
  - Left-click to start drawing.
  - Left-click again to finish the shape.
     ###insert "C:\Users\isaac\Downloads\KuasaSemi\aquarius-docs\static\img\examples\PN junction\p_region\02.png"
- After drawing the rectangle, the Exact Coordinates dialog will open automatically:
  - Set the First Vertex to (-0.1, 0).
  - Set the Second Vertex to (0.1, 1).
  - Click OK to confirm.
###insert "C:\Users\isaac\Downloads\KuasaSemi\aquarius-docs\static\img\examples\PN junction\p_region\03.png"

- The Region Properties dialog will then open:
  - Set the Region Material to Silicon (Si);
  - Set the Acceptor Doping to 1E+16
  - Click OK to confirm.
##insert "C:\Users\isaac\Downloads\KuasaSemi\aquarius-docs\static\img\examples\PN junction\p_region\04.png"
- Repeat process again but changing the colour of the region and this time with the following parameters:
  - Set the First Vertex to (-0.1, 0.1).
  - Set the Second Vertex to (1, 2).
  - Set Donner concentration to 1E+16.
  - Select a colour of choice for the N region. It is better to have it set as a different region to the P region for differentiability.
Note: the two regions should be neatly on top of each other.
### Insert "C:\Users\isaac\Downloads\KuasaSemi\aquarius-docs\static\img\examples\PN junction\n_region\07.png"
4.1.3	Define device contacts
***Copy and past define contacts in resistor example but add my images
4.1.4	Defining mesh construction lines
As it was done in the simple resistor example, an initial grid is defined. Here the mesh will be slightly different as we are simulating a PN diode which is slightly more complex than a resistor. In this example of a PN diode, It is necessary to have fixed vertical mesh and a graded horizontal mesh. The horizontal mesh should be graded in such a way that the spacing between the lines increases towards the depletion region at the centre of the diode. This is because the centre of the diode is a point of interest.